# sinusoidal steady-state analysis

List of topics for this chapter :

Nodal Analysis

Mesh Analysis

Superposition Theorem

Source Transformation

Thevenin and Norton Equivalent Circuits

AC Op Amp Circuits

nodal Analysis

## Given the circuit in Figure 10.1 and  amps, find  using nodal analysis.

Figure 10.1

Carefully DEFINE the problem.

Each component is labeled, indicating the value and polarity.  The problem is clear.

PRESENT everything you know about the problem.

The goal of the problem is to find , which is clearly labeled in Figure 10.1, using nodal analysis.  Thus, we need to label the nodes and ground.

To find  without using derivatives and integrals, we must transform the circuit to the frequency domain.  This allows us to find the answer using algebra with complex numbers.  We can transform the circuit to the frequency domain after setting a reference value.  Let us use a reference of .

In transforming to the frequency domain, remember that  and .  Hence, the inductor becomes  and the capacitor becomes .

Let us draw the circuit after the transformation into the frequency domain and labeling the nodes and ground.

Establish a set of ALTERNATIVE solutions and determine the one that promises the greatest likelihood of success.

The problem clearly states that the problem be solved using nodal analysis.  Thus, the technique to solve the problem is set.  There is no reason to look at an alternative at this point.

ATTEMPT a problem solution.

Let us begin by writing the node equations.

At node 1 :					At node 2 :

Simplifying,

Thus, the system of simultaneous equations is

So,

or	 volts

or	 volts

Clearly,

and 	  amps

Hence,

volts

Therefore,

volts

EVALUATE the solution and check for accuracy.

Solving the problem with an alternate method, such as mesh analysis in this case, would show that the results of the problem solution are correct.

Let us draw the circuit defining the loop currents for mesh analysis.

Write the loop equations.

Loop 1 :	 amps

Loop 2 :

Loop 3 :

Simplifying the equations for loops 2 and 3,

Loop 2 :

Loop 3 :

Solve the third loop equation for  in terms of .

Now, substitute  and  into the second loop equation and simplify to find .

amps

Now, find .

amps

Clearly,  amps.

Evidently,

volts

and 	 volts

This answer is the same as the answer obtained using nodal analysis.  Our check for accuracy was successful.

Has the problem been solved SATISFACTORILY?  If so, present the solution; if not, then return “ALTERNATIVE solutions” and continue through the process again.

This problem has been solved satisfactorily.

## [10.5]	Given the circuit in Figure 10.2 and  volts, use nodal analysis to find .

Figure 10.2

Let us start by building the ac circuit.  The voltage source, volts, becomes volts, with .  The inductive reactance becomes .  The capacitive reactance becomes .  Now, draw the ac circuit.

At node 1 :					At node 2 :

Note that  was substituted when writing the equation for node 2.

Substituting the equation for node 2 into the equation for node 1,

or

Clearly,

volts

With a reference of ,

## Given the circuit in Figure 10.3 and  volts, find  using nodal analysis.

Figure 10.3

mesh analysis

## Given the circuit in Figure 10.4 and  amps, find  using mesh analysis.

Figure 10.4

First, we transform the circuit to the frequency domain using a reference of  and define the mesh currents as seen in the following circuit.

Remember that  and .

There is only one unknown loop current, .

Writing the loop equation,

amps

Therefore,

## Given the circuit in Figure 10.5 and  amps, find  using mesh analysis.

Figure 10.5

Transform the circuit to the frequency domain using a reference of  and define the mesh currents.

Clearly, .

Use mesh analysis to find  and .

For loop 1 :

For loop 2 :

Simplifying,

Simplifying further,

Find  in terms of  for the second loop equation.

Substituting this equation into the first loop equation we get,

Hence,

amps

Therefore,

superposition theorem

The superposition theorem applies to ac circuits the same as it does for dc circuits.  This theorem is important if the circuit has sources operating at different frequencies.  Since the impedances depend on frequency, we must have a different frequency-domain circuit for each source.  The total response is obtained by adding the individual responses in the time domain.

## Given the circuit in Figure 10.6,  amps and  volts, find .

Figure 10.6

Because the two sources have different frequencies, we need to use superposition to solve this problem.  Thus, .

Start with the current source and a reference of .

Using current division,

amps

Hence,

amps

Next, use the voltage source with a reference of .

Clearly,

amps

Hence,

amps

Recall that .

Therefore,

## [10.33]	Given the circuit in Figure 10.7 and  volts, solve for  using the principle of superposition.

Figure 10.7

Let  where , , and  are respectively the voltages produced by the 10 volt dc source, the ac current source, and the ac voltage source acting independently.  For , consider the circuit shown in Figure (a).

The capacitor is an open circuit to dc while the inductor is a short circuit.  Hence,  volts and  volts.

For , consider the circuit in Figure (b).  , so the inductor becomes .  Likewise, the capacitor becomes .

Applying nodal analysis,

which leads to

volts

With a reference of ,

volts

For V3, consider the circuit in Figure (c).   which leads to  for the inductor and  for the capacitor.

At the non-reference node,

which leads to

volts

With a reference of,

volts

Recall that .

Therefore,

## Given the circuit in Figure 10.8 and  volts, find .

Figure 10.8

or

source transformation

Source transformation in the frequency domain involves transforming a voltage source in series with an impedance to a current source in parallel with an impedance or vice versa.  We must keep the following relationship in mind when performing source transformations.

## Given the circuit in Figure 10.9 and  volts, find  using source transformations.

Figure 10.9

Transform the circuit to the frequency domain using a reference of .

Reduce the circuit using source transformations.  Begin with the 20(0(V source in series with 6( which becomes a 10/3(0(A source in parallel with 6(.

Now combine 6( || 8(  =  24/7(.  The 10/3(0(A source in parallel with 24/7( becomes an 80/7(0(V source in series with 24/7(.

To perform the next source transformation, we need to find the parallel equivalent of the resistor and capacitor in series.  We know that two series impedances and two parallel impedances are

and

To find the parallel equivalence of two series impedances, let .  Then,

It can be shown that

Thus, the 80/7(0(V source in series with 24/7 – j4( becomes a 2.169(49.4(A source in parallel with 8.095 – j6.939(.

Combining 8.095( || 20(  =  5.763(.  We now need to find the series equivalent of the resistor in parallel with the capacitor.  It can be shown that

Thus, the 2.169(49.4(A source in parallel with 5.763 – j6.939( becomes a 9.618(9.69(V source in series with 3.411 – j2.833(.  Before redrawing the circuit, let’s combine the series resistances of 3.411( + 10(  =  13.411(.

Now that we have found a less complex circuit via source transformations, it is simple to solve for .

and

Recall that we used a reference of .  Therefore,

Thevenin and Norton Equivalent Circuits

## Given the circuit in Figure 10.10 and  volts, find , , and  looking into terminals a and b.

Figure 10.10

Because the circuit in Figure 10.10 has a capacitor, we can only determine , , and  for an ac circuit in the frequency domain.  Hence, the circuit becomes,

Begin by finding the open-circuit voltage,.  Note that there is no current flowing through the capacitor.  Thus, .

Using nodal analysis,

where .

So,

volts

Hence,

volts

Now, find the short-circuit current, .

Use nodal analysis to find  and then

Writing the nodal equation,

where .

So,

Thus,

amps

Finally,

ohms

Therefore,

or

or

or

## [10.43]	Find the Thevenin and Norton equivalent circuits for the circuit shown in Figure 10.11.

Figure 10.11

To find , consider the circuit shown in Figure (a).

ohms

To obtain , consider the circuit in Figure (b).

volts

amps

where  is the current flowing downward through a short across the terminals.

Recall that , , and .

Therefore,

## Given the circuit in Figure 10.12 and  volts, find , the current through R, for .

Figure 10.12

A

A

A

A

A

AC Op Amp Circuits

## Given the ac circuit in Figure 10.13, find  as a function of .

Figure 10.13

Using nodal analysis at node a,

where .

So,

Therefore,

The output is equal to the input except for a phase shift of 90(.

## Given the circuit in Figure 10.14 and  volts, find  for rad/sec.

Figure 10.14

Use the following ac circuit, with a reference of , to find  in terms of (.

Using nodal analysis at node a,

where .

So,

Now, substitute the values for ( into the equation for .

At  rad/sec,

At  rad/sec,

At  rad/sec,

This corresponds to the case where the LC combination forms a parallel resonant circuit and the output goes to infinity.

At  rad/sec,

In conclusion, the output,, has a –90( phase shift for all values of ( less than 100 and has a 90( phase shift for values of ( greater than 100.

# Text boxes

#### 10 (

##### +

##### vo(t)

##### (

### 10 mH

### 50 (F

#### 10 (

### 30 (

##### i(t)

#### 10 (

##### +

##### Vo

##### (

### j10 (

### –j20 (

#### 10 (

### 30 (

##### 5(0( A

#### V1

#### V2

#### Io

### 8 (

#### 6 (

### 20 (

### 10 mH

#### 10 (

##### +

##### Voc

##### (

#### io(t)

+

(

##### v(t)

+

(

##### 12(0( V

##### +

##### V3

##### (

#### j6 (

#### 6 (

+

(

### –j4 (

#### (c)

### 4(0( A

##### +

##### V2

##### (

#### io(t)

### 20 mH

### 10 (

#### 10 (

##### i(t)

##### i(t)

#### 10 (

#### io(t)

### 10 mH

#### Io

### 50 (F

### j20 (

### 10 (

#### 10 (

##### 2(0( A

#### 10 (

### 30 (

##### 5(0( A

#### 10 (

### j10 (

### –j20 (

#### 10 (

### 30 (

#### I2

#### I1

#### Io

#### 20 (

#### iC(t)

### 50 (F

##### i(t)

### v(t)

+

(

#### 20 (

#### IC1

### –j20 (

##### 2(0( A

#### IC2

### 20 (

##### –j15 (

### 20 mH

### 10(0( V

+

(

#### 50 (F

#### 20 (

#### v(t)

+             (

### vS(t)

+

(

##### 10 V

+

(

#### j4 (

#### 6 (

### –j6 (

#### (b)

#### (a)

##### +

##### V1

##### (

#### 250 (F

### 10 V

+

(

#### 2 H

#### 6 (

### 1/12 F

##### +

##### vo(t)

##### (

### 10 V

+

(

### 4sin(2t) A

#### 2 H

#### 6 (

##### vi(t)

##### +

##### vo(t)

##### (

+

(

##### v(t)

### 20 (

#### 10 (

### 10 mH

#### 6 (

### 8 (

##### +

##### Vo

##### (

#### –j4 (

+

(

##### 10/3(0( A

### 20 (

#### 10 (

### j10 (

#### 6 (

### 8 (

##### 20(0( V

##### +

##### Vo

##### (

#### –j4 (

### 6 (

### 20 (

#### 10 (

### j10 (

### 8.095 (

### 8 (

##### 2.169(49.4(A

##### +

##### Vo

##### (

#### 5 (

### 20 (

#### 10 (

### j10 (

### –j6.939 (

##### 80/7(0( V

##### +

##### Vo

##### (

#### –j4 (

+

(

### 20 (

#### 10 (

### j10 (

#### 24/7 (

##### +

##### Vo

##### (

### 3i(t)

+

(

+

(

#### I

### j10 (

#### 13.411 (

#### b

#### a

#### 1 mF

#### 250 (F

### 5 (

### i(t)

##### v(t)

##### 9.618(9.69(V

### 3I

#### Io

##### 10(0( V

#### –j (

### 5 (

### I

#### V1

#### 5 (

+

(

##### 100(0( V

#### V1

##### 100(0( V

### 3I

### 4Io

+

(

#### –j (

### 5 (

### I

#### 5 (

+

(

#### Isc

#### 5 (

### 50 (F

#### 10 mH

#### 10 (

##### v(t)

+

(

### R

### 1/12 F

##### +

##### Vo

##### (

### 30 (

### 20 (

#### j10 (

#### –j20 (

+

(

#### 20 (

### +

### Voc

### (

#### V1

#### V2

#### –j2.833 (

### 4io(t)

##### +

##### vo(t)

##### (

### 30 (

### 20 (

#### 10 mH

##### +

##### Vout

##### (

#### 50 (F

##### vi(t)

#### 1 k(

+

(

#### 20 (

#### –j1000 (

#### Vb

#### Va

(

+

### 10 (

##### Vin

+

(

### 10 (

##### +

##### Vout

##### (

##### 10(0(

+

(

#### 104 (

#### –j105/( (

#### Vb

#### Va

(

+

#### j10( (

#### 10 H

### 10 (

##### +

##### vout(t)

##### (

##### vin(t)

+

(

#### 10 k(

#### 10 (F

#### Vb

#### Va

(

+

##### 60(120( V

#### 2 (

### j20 (

#### –j10 (

#### 5 (

##### (b)

#### 2 (

### j20 (

#### –j10 (

#### 5 (

##### (a)

#### Zeq

+

(

##### 60(120( V

#### 2 (

### j20 (

#### –j10 (

#### 5 (

#### io(t)

#### Io

#### I1

#### I3

#### 10 (

##### +

##### Vo

##### (

### j10 (

### –j20 (

#### 10 (

### 30 (

##### 5(0(

#### I2

#### io(t)