Chapter 15

constraint management: Simplifying complex systems

Solutions to Odd-Numbered End-of-Chapter Problems

1. 
a. One unit every 8 minutes

b.

| wc1 | 0.625 |
| --- | --- |
| wc2 | 0.875 |
| wc3 | 0.75 |
| wc4 | 0.625 |
| wc5 | 1 |

3.

a. In front of WC1 and WC3

b.  Using the constraint management definition for utilization,

| wc1 | 0.875 |
| --- | --- |
| wc2 | 0.75 |
| wc3 | 1 |
| wc4 | 1 |
| wc5 | 0.75 |
| wc6 | 0.875 |

5.  The process is capable of operating at 15 apples per minute or 900 apples per hour.

7. The first workstation is the constraint and would therefore be utilized 100%.

| Work Station | Time | Utilization |
| --- | --- | --- |
| Add Ground beef | 20 | 100.00% |
| Add lettuce | 18 | 90.00% |
| Add cheese | 12 | 60.00% |
| Add tomatoes | 9 | 45.00% |
| Package | 15 | 75.00% |

9.

|  | Product | Required | Required | Required |
| --- | --- | --- | --- | --- |
|  | Demand | Time on | Time on | Time on |
|  |  | Molding | Coloring | Cutter |
| Wiffle Bat | 190 | 1900 | 950 | 0 |
| Wiffle Ball | 125 | 625 | 0 | 625 |
|  | Total | 2525 | 950 | 625 |
|  | Available | 2400 | 2400 | 2400 |

Molding is the constraint. Not all demand can be met.

With the engineering change all demand can be met, so yes, the engineering change should be done.

|  | Product | Required | Required | Required |
| --- | --- | --- | --- | --- |
|  | Demand | Time on | Time on | Time on |
|  |  | Molding | Coloring | Cutter |
| Wiffle Bat | 190 | 1710 | 1900 | 0 |
| Wiffle Ball | 125 | 625 | 0 | 625 |
|  | Total | 2335 | 1900 | 625 |
|  | Available | 2400 | 2400 | 2400 |

11.

|  | Product | Required | Required | Required | Required |
| --- | --- | --- | --- | --- | --- |
|  | Demand | Time on | Time on | Time on | Time on |
|  |  | Cutter | Sewing | Dye | Logo |
| Shirt 001 | 70 | 1260 | 1680 | 0 | 0 |
| Shirt 004 | 50 | 950 | 1300 | 1750 | 600 |
|  | Total | 2210 | 2980 | 1750 | 600 |
|  | Available | 2400 | 2400 | 2400 | 2400 |

The constraint is sewing.  Produce 45 of Shirt 001 and 50 of shirt 004.