# Quiz 1 Solution			 	40 minutes

1.  (5)  Convert the decimal number 113 to binary.  Show your work.

113/2  =  56	r = 1				1

56/2	= 28		r = 0				01

28/2  =  14		r = 0				001

14/2  =  7		r = 0				0001

7/2  =  3		r = 1				10001

3/2  =  1		r = 1				110001

1/2  =  0		r = 1				1110001	ANSWER

2.  (10)  a)  Add the two pairs of binary numbers and show the results in binary.   (Be sure to show the carry as you add.)

0 1 1 1

0 0 1 0 1

1 0 1 1 1

1 1 1 0 0

b)  Show both operands and the result of the addition in decimal if the numbers are

i)  unsigned			 ii) signed (two's complement)

5  +  23  =  28				5  +  (-9)  =  -4

3.  (10)  Each of the following 8-bit numbers was found in a computer.  Show the decimal equivalent (if it exists) if each is

0 0 0 1  0 1 1 0		1 1 0 0  1 0 1 0

a)  unsigned binary			22			202

b)  signed binary				+22			-54

c)  BCD (8421 code)			16		not a number

4.  (10)  Complete the truth table for a system with 3 inputs, a, b,  and c, and 4 outputs, w, x, y, z.  The output is a binary number equal to the smallest integer that meets the input conditions:

a = 0:  odd				a = 1:  even

b = 0:  prime			b = 1:  not prime

c = 0:  less than 8		c = 1:  greater than or equal to 8

Some inputs may never occur; the output is never all 0's.

(A prime is a number that is only evenly divisible by itself and 1.)

To be sure you understand the problem, I have completed one output row.

| a | b | c | w | x | y | z |
| --- | --- | --- | --- | --- | --- | --- |
| 0 | 0 | 0 | 0 | 0 | 0 | 1 |
| 0 | 0 | 1 | 1 | 0 | 1 | 1 |
| 0 | 1 | 0 | X | X | X | X |
| 0 | 1 | 1 | 1 | 0 | 0 | 1 |
| 1 | 0 | 0 | 0 | 0 | 1 | 0 |
| 1 | 0 | 1 | X | X | X | X |
| 1 | 1 | 0 | 0 | 1 | 0 | 0 |
| 1 | 1 | 1 | 1 | 0 | 0 | 0 |

5.  (15)  Reduce the expression below (using the algebraic properties) to a sum of products expression with 2 terms and 3 literals.  Show each step.

x' y' z'  +  x' y' z  +  x' y z'  +  x' y z  +  x y z'

=	x' y' (z' + z)  +  x' y (z' + z)  +  x y z'

=	x' y'  +  x' y  +  x y z'

=	x' (y' + y)  +  x y z'

=	x'  +  x y z'			[a  +  a’ b  =  a  +  b]

=  	x'  +  y z'