Quiz 6 Solution			 	60 minutes

Blank Maps for first three problems provided on page 4, but write answers on the page with the problem statement.

1.  For the following state table,

|  | q1 q2 | q1* | q2* |  | z |
| --- | --- | --- | --- | --- | --- |
|  |  | x = 0 | x = 1 | x = 0 | x = 1 |
|  | 0 0 | 0 1 | 1 1 | 0 | 1 |
|  | 0 1 | 0 0 | 1 0 | 0 | 0 |
|  | 1 0 | 1 1 | 1 0 | 0 | 1 |
|  | 1 1 | 0 0 | 1 1 | 0 | 1 |

Show the flip flop input equations and the output equation if the first flip flop is a D flip flop and the second is JK.

D1			   q2*			    z

D1  =  x  +  q1 q2'

J2  =  x'  +  q1'

K2  =  x'  +  q1'

z  =	x (q1 + q2')

2.  For the following state table and state assignment, show the equations and a block diagram for a system using an SR flip flop for q1 and a T flip flop for q2 and AND, OR and NOT gates.  (Show only one of the solutions for R1.)

|  | q | q | * |  | z |  | q | q1 q2 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | x=0 | x=1 | x=0 | x=1 |  | A | 1 0 |
|  | A | B | C | 1 | 1 |  | B | 0 1 |
|  | B | A | B | 1 | 0 |  | C | 1 1 |
|  | C | B | A | 1 | 0 |  |  |  |

|  | x | q1 | q2 | q1* | q2* | z | S1 | R1 | T2 |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| - | 0 | 0 | 0 | X | X | X | X | X | X |  |  |
| B | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 |  | S1 = x' q1' |
| A | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 |  |  |
| C | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0 |  | R1 = x' q1 |
| - | 1 | 0 | 0 | X | X | X | X | X | X |  |  |
| B | 1 | 0 | 1 | 0 | 1 | 0 | 0 | X | 0 |  | T2 = q2' + x' q1' |
| A | 1 | 1 | 0 | 1 | 1 | 1 | X | 0 | 1 |  | + x q1 |
| C | 1 | 1 | 1 | 1 | 0 | 0 | X | 0 | 1 |  | z = x' + q2' |

3.   Design a counter that goes through the sequence

1   0   7   3   4   2   and repeat

using a D flip flops.  Just show the equations.

|  | A | B | C | A* | B* | C* |
| --- | --- | --- | --- | --- | --- | --- |
|  | 0 | 0 | 0 | 1 | 1 | 1 |
|  | 0 | 0 | 1 | 0 | 0 | 0 |
|  | 0 | 1 | 0 | 0 | 0 | 1 |
|  | 0 | 1 | 1 | 1 | 0 | 0 |
|  | 1 | 0 | 0 | 0 | 1 | 0 |
|  | 1 | 0 | 1 | X | X | X |
|  | 1 | 1 | 0 | X | X | X |
|  | 1 | 1 | 1 | 0 | 1 | 1 |

DA  =  A' B' C'  +  A' B C

DB  =  A  +  B' C'

DC  =  A' C'  +  {A B  or  A C}

BONUS:  Show a state diagram, including what happens if the system begins in state 5 or 6.

101 ->  0 1 0   or   0 1 1

110 ->  0 1 1   or   0 1 0

4.  Show a state table or a state diagram for a system with one input, x, and one output, z, such that z = 1 if and only if the input has been at least three consecutive 1's followed by two 0's.  (Full credit for a system with 5 states.)

Example

x	1   1   1   1   0   0   0   1   1   0   0   1   1   1   0   0

z	0   0   0   0   0   1   0   0   0   0   0   0   0   0   0   1   0   0

|  | q | q | * | z |  |
| --- | --- | --- | --- | --- | --- |
|  |  | x = 0 | x = 1 | x = 0 | x = 1 |
|  | A | A | B | 0 | 0 |
|  | B | A | C | 0 | 0 |
|  | C | A | D | 0 | 0 |
|  | D | E | D | 0 | 0 |
|  | E | A | B | 1 | 0 |