Solution to every third end-of-chapter problem

Basics of Engineering Economy, 2nd edition

Leland Blank and Anthony Tarquin

# Chapter 11

Estimating Costs

11.1   	Elements of first cost include equipment cost, delivery charges, installation cost,

insurance coverage, and training of personnel for equipment use.

11.4   	Cost = 98.23(50,000) = $4,911,500

11.7   	Cost = 1,350,000(1.70/0.93) = $2,467,742

11.10  	Cost = 185,000(1634.9/1375.4) = $219,904

11.13   From Table, index value in 2003 = 6695; index value in 2012 = 9290

Ct = 30,000,000(9290/6695)

= $41,628,000

11.16    Cost2011 = Cost2002(1490.2/1104.2)

328 = Cost2002(1.3496)

Cost2002 = $243

11.19         31.39 = Rate1913(16,520.53/100)

Rate1913 = $0.19 per hour

11.22   C2 = 9500(450/250)0.32

= 9500(1.207)

# = $11,466

11.25	If C2 = 1.04 C1 and Q2/Q1 = 0.50, the cost-capacity relation is

1.04C1 = C1 (Q2/Q1)x

1.04 = (0.50)x

log 1.04 = x log 0.50

x = -0.0566

11.28   Cost = 3750(2)0.89(1520.6/1104.2) = $9570

11.31    1,320,000 = h(225,000)

h = 5.87

11.34   T12 = T1Ns

s = log 0.85/log 2

= -0.234

T12 = (56)12-0.234

= 31.3 months

11.37   Total direct labor hours = 3000 + 9000 + 5000

= 17,000 hours

Indirect cost/hour = 34,000/17,000

= $2.00

Allocation to Dept A = 3000(2.00)

= $6000

Allocation to Dept B = 9000(2.00)

= $18,000

Allocation to Dept C = 5000(2.00)

= $10,000

11.40   (a) Hand solution:  Make alternative indirect cost computation

| Dept | Rate (1) | Usage (2) | Annual cost (3) = (1)(2) |
| --- | --- | --- | --- |
| M | $2.40 | 450,000 | $1.08 million |
| P | $0.50 | 850,000 | 425,000 |
| Q | $25 | 4800 | 120,000 |
| $/year |  |  | $1,625,000 |

Determine AW for make and buy alternatives.

# AWmake = -3,000,000(A/P,12%,6) + 500,000(A/F,12%,6)

# – 1,500,000 – 1,625,000

= -3,000,000(0.24323) + 500,000(0.12323) – 3,125,000

= $-3,793,075

AWbuy = -4,500,000 – 200,000(A/G,12%,6)

= -4,500,000 – 200,000(2.1720)

= $-4,934,400

# Select make alternative.

# (b) Spreadsheet solution: Select to make inhouse.

11.43	Compare last year’s allocation based on flight traffic with this year’s based on

baggage traffic. Significant change took place.

|  | Last year; flight basis | This year; baggage basis | Percent change |
| --- | --- | --- | --- |
| DFW | $330,000 | $343,620 | + 4.1% |
| YYZ | 187,500 | 218,371 | +16.5 |
| MEX | 150,000 | 105,363 | – 29.7 |

11.46   The answer is (c)

11.49   C2 = 22,000(300/200)0.64 = $28,518

Answer is (b)

11.52   CT = 2.45(390,000) = $955,500

# Answer is (a)

11.55      3,000,000 = 550,000(100,000/6000)x

5.4545 = (16.67)x

log 5.4545 = xlog16.67

x = 0.60

Answer is (d)

11.58   Allocation = (900 + 1300)(2000) = $4.4 million

Percent allocated = 4.4/8.0 million = 55%

Answer is (c)